The following is a news release from Master Bond Inc. You have received it because you are listed as an editor for your publication.

Attached to this email is a low resolution version of the photograph that is included in the press kit for this product.

High resolution version of this image and files with the body text of this release in Word, HTML and text formats are available at http://www.masterbond.com/newsrelease/ep3hts-lo.

-----------------------------------------------------------------

## FOR IMMEDIATE RELEASE

One Part, Electrically Conductive Epoxy Meets NASA Low Outgassing Specifications

Master Bond EP3HTS-LO is a single component epoxy for demanding bonding, sealing and coating applications. This system passes ASTM E595 tests for NASA low outgassing, making it well suited for use in the aerospace, electronic, microelectronic and optical industries.

Featuring a silver filler, EP3HTS-LO is electrically conductive with a low volume resistivity of less than 0.001 ohm-cm. It also has a thermal conductivity of 12-15 BTU•in/(ft²•hr•°F) [1.73-2.16 W/(m·K)]. EP3HTS is dimensionally stable and bonds well to metals, glass, composites, ceramics and many plastics. It withstands a variety of chemicals such as water, oils, fuels and cleaning agents. This high temperature resistant system is serviceable over the wide temperature range of -60°F to +400°F.

As a one part compound, EP3HTS-LO offers convenient handling with no mixing and an unlimited working life at room temperature. This smooth thixotropic paste can be readily dispensed from a syringe. It polymerizes quickly at elevated temperatures with cure schedules of 45-50 minutes at 250°F or 20-30 minutes at 300°F.

EP3HTS-LO is available for use in glass jars and syringes. It has a minimum shelf life of 3 months and a maximum of 6 months at ambient temperatures in its original, unopened containers.

Master Bond Silver Conductive Adhesives

NASA low outgassing approved, Master Bond EP3HTS-LO is a single component compound that cures rapidly at elevated temperatures. It offers superior dimensional stability, thermally conductivity and electrical conductivity. Read more about Master Bond’s silver filled, electrically conductive adhesives at www.masterbond.com/properties/silver-filled-electrically-conductive-adhesives or contact Tech Support. Phone: +1-201-343-8983 Fax: +1-201-343-2132 Email: technical@masterbond.com.

Note to Editors:

For a full product description, please visit: http://www.masterbond.com/tds/ep3hts-lo

Check out new videos on our YouTube channel: http://www.youtube.com/user/MasterBondVideo

You can embed any of our videos on your website.

CONTACT

James Brenner, Marketing Manager

Email: jbrenner@masterbond.com

Tel: +1-201-343-8983

Fax: +1-201-343-2132

MASTER BOND INC.

154 Hobart Street

Hackensack, NJ 07601-3922

Web: www.masterbond.com

# # #